## Slide 1: Topic 07 – Equilibrium 7.2: Position of Equilibrium and Le Chatelier’s Principle
IB Chemistry
T07D02

## Slide 2: 7.2 The position of equilibrium - 4 hours
7.2.1 Deduce the equilibrium constant expression (Kc) from the equation for a homogeneous reaction. (3)
7.2.2 Deduce the extent of a reaction from the magnitude of the equilibrium constant. (3)
7.2.3 Apply Le Chatelier’s principle to predict the qualitative effects of changes of temperature, pressure and concentration on the position of equilibrium and on the value of the equilibrium constant. (2)
7.2.4 State and explain the effect of a catalyst on an equilibrium reaction. (3)
    7.2.5 Apply the concepts of kinetics and equilibrium to industrial processes. (2)

## Slide 3: 7.1 – Summation of last class
Dynamic Equilibrium is in a closed system, no loss or gain of material
Amounts of reactants and products remain constant
Dynamic, not static equilibrium. They undergo both forward and reverse reactions
The rates of forward & reverse reactions are equal
Equilibrium can be achieved from either direction (starting with the left or right side of the equation)
We will study reactions in homogeneous equilibria, meaning they are all in the same physical phase.

## Slide 4: 7.2.1 – Equilibrium Constant (Kc)
7.2.1 Deduce the equilibrium constant expression (Kc) from the equation for a homogeneous reaction. (3)
The position of the equilibrium for a particular reversible reaction can be defined by a constant, Kc
For the general reaction:
  aA + bB ⇌ cC + dD
Products on top
‘powers’ are coefficients
Multiple materials are multiplied
[brackets] = conc mol dm-3

## Slide 5: 7.2.1 – Equilibrium Law
Kc is for a given temperature, if the temperature changes then the value of Kc does as well
The general expression of Kc is known as the equilibrium law which can be adapted to particular equations to be studied in equilibrium

## Slide 6: 7.2.1 – Kc Example with Ammonia
N2(g) + 3H2(g) ⇌ 2NH3(g) @500oC
From Table:
  Find Kc for each
  Exp. 1
  Exp. 2
  Exp. 3
 | [N2] (M) | [H2] (M) | [NH3] (M)
Ex. 1 | 0.992 | 0.763 | 0.157
Ex. 2 | 0.299 | 1.197 | 0.203
Ex. 3 | 2.59 | 2.77 | 1.82

## Slide 7: 7.2.1 – Kc for Reversible Reactions
For the forward reaction:
  H2(g) + I2(g) ⇌ 2HI(g)
For the reverse reaction:
  2HI(g) ⇌ H2(g) + I2(g)
or Kc-1

## Slide 8: 7.2.1 – Kc from either side
A series of experiments @ 700oC returns a value of Kc of 54 regardless of the starting point of reaction or initial concentrations
  H2(g) + I2(g) ⇌ 2HI(g)
  2HI(g) ⇌ H2(g) + I2(g)
 | [H2] (10-3 M) | [I2] (10-3 M) | [HI] (10-3 M) | Kc
Ex. 1 | 4.56 | 0.74 | 13.49 | 54
Ex. 2 | 3.56 | 1.25 | 15.50 | 54
Ex. 3 | 2.25 | 2.34 | 16.86 | 54
 | [H2] (10-3 M) | [I2] (10-3 M) | [HI] (10-3 M) | Kc` | Kc (1/Kc`)
Ex. 1 | 0.48 | 0.48 | 3.52 | 0.0186 | 54
Ex. 2 | 0.50 | 0.50 | 3.67 | 0.0186 | 54

## Slide 9: 7.2.1 - Practice
Write the equilibrium Expression for the following reversible reactions. Each are homogeneous equilibria
  2SO2(g) + O2(g) ⇌ 2SO3(g)
  Fe3+(aq) + SCN-(aq) ⇌ [Fe(SCN)]2+
  4NH3(g) + 5O2(g) ⇌ 4NO(g) + 6H2O(g)

## Slide 10: 7.2.1 – Calculate revers Kc
The following reaction is an esterification reaction producing ethyl ethanoate:
  CH3CO2H(l) + C2H5OH(l) ⇌ CH3CO2C2H5(l) + H2O(l)
The value of Kc for this reaction is 4.0 @ 25oC
This equilibrium can be approached from the reverse reaction, find the Kc of that reaction:

## Slide 11: 7.2.2 – Meaning of the Magnitude of Kc
7.2.2 Deduce the extent of a reaction from the magnitude of the equilibrium constant. (3)
The magnitude of Kc gives us an indication of how far a reaction has gone towards completion under the given conditions
If Kc is high = equilibrium “lies to the right”
  H2(g) + Cl2(g) ⇌ 2HCl(g) Kc = 1018 @ 277oC
If Kc is low = equilibrium “lies to the left”
  H2(g) + I2(g) ⇌ 2HI(g) Kc = 2 @ 277oC
  Bonding in HI is weaker than in HCl. HCl doesn’t readily decompose in heat, where HI does.
  Reaction to form HCl goes virtually to completion

## Slide 12: 7.2.2 – Relative Kc values
As a general rule:
  If Kc >> 1 then the reaction is said to go to completion
  If Kc << 1 then the reaction has hardly taken place at all
  The equilibrium constant indicates the extent of a reaction at a particular temperature.
  It gives no indication of how fast equilibrium is achieved.
Reaction hardly goes | “Reactants” dominate at Equilibrium | Reactants equal Products | “Products dominate at Equilibrium | Reaction virtually goes to completion
Kc < 10-10 | Kc = 0.01 | Kc = 1 | Kc= 100 | Kc > 1010

## Slide 13: 7.2.2 – Alterations to Kc
Kc is NOT altered by:
  The addition/removal of products/reactants
  Change in pressure
  Addition of a catalyst
Remember, it’s the concentration, not the amount
  If you take away 0.100L of 1.00L solution of 2.0M NaOH, you still have 2.0M NaOH left, just in less volume
The Kc for a given reversible reaction at equilibrium only changes if the temperature changes

## Slide 14: 7.2.2 – Chromate and Dichromate
2CrO42-(aq) + H+(aq) ⇌ Cr2O72-(aq) + OH-(aq)
Yellow Orange
  The shifts are easily seen by a change in color of the ions involved
  Potassium (VI) dichromate is yellow when dissolved
    Addition of acid pushes reaction to the left to start off at equilibrium, further H+ pushes the reaction to the right
  Potassium (VI) chromate is orange when dissolved
    This solution favors a solution of low pH

## Slide 15: 7.2.3 – Le Chatelier’s Principle
7.2.3 Apply Le Chatelier’s principle to predict the qualitative effects of changes of temperature, pressure and concentration on the position of equilibrium and on the value of the equilibrium constant. (2)
“When a system at equilibrium is disturbed, the equilibrium position will shift in the direction which tends to minimize, or counteract, the effect of disturbance.”
-Henri Louis Le Chatelier (1850-1936)

## Slide 16: 7.2.3 – What does it mean?
If conditions at which equilibrium have been established change, the position of equilibrium is effected.
Le Chatelier’s principal describes what happens when the dynamic equilibrium is disturbed but does not explain why
  The system responds to negate the change
    If more reactant is added, the system will react to remove it
    If product is taken away, the system will act to replace it

## Slide 17: 7.2.3 – Effects on position and Kc
Possible changes in conditions to consider:
  Changes in [conc] of reactants or products
  Changes in pressure for gas phase reactions
  Changes in temperature
  The presence of a catalyst
Change Made | Effect on ‘position of equilibrium’ | Value of Kc
[conc] of one of the components in the mixture | Changes | Remains unchanged
Pressure | Changes if the reaction involves a change in the total # of gas particles | Remains unchanged
Temperature | Changes | Changes
Use of a catalyst | No change | Remains unchanged

## Slide 18: 7.2.3 – Changes in [conc]
Again, consider the esterfication reaction:
CH3CO2H(l) + C2H5OH(l) ⇌ CH3CO2C2H5(l) + H2O(l)
Ethanoic acid ethanol ethyl ethanoate water
  If we remove water, then more of the reactants will react to replace it, producing more ester and water
Step 2: equilibrium is shifted to the right
Step 1: Product is removed

## Slide 19: 7.2.3 – Production of Ammonia
A very important industrial process is the production of ammonia (NH3)
  N2(g) + 3H2(g) ⇌ 2NH3(g)
  When the reaction is in dynamic equilibrium, the concentrations are constant
  If excess N2(g) is added, the equilibrium at first is no longer stable
  To return to equilibrium, more NH3 is produced
  Check out the following graphs on the next slide

## Slide 20: 7.2.3 – Equilibrium Shift for NH3 production with addition of reactant
Concentration / mol dm-3
Time
[N2]
[NH3]
[H2]
Concentration / mol dm-3
Time
[N2]
[NH3]
[H2]
Eq. initial
Eq initial
Addition of excess N2
New Eq
In general:
  Increasing [reactant] shifts equilibrium to the right
  Increasing [product] shifts equilibrium to the left

## Slide 21: 7.2.3 – Change in Pressure
Pressure only affects gaseous reactions
There is a direct relationship between the number of molecules of gas present and the pressure it exerts on its container
If pressure is increased, the system will favor the side of the reaction with less molecules
  In doing so the pressure of the mixture will be reduced
Yes, this is a change volume, but in effect it’s a change in pressure
+ ⇌

## Slide 22: 7.2.3 – Pressure of N2O4
Useful reaction to study for change in pressure:
  N2O4(g) ⇌ 2NO2(g)
  colorless brown
  The equilibrium can easily be monitored by a change in color
  Pressure is increased:
    Initially darkens the solution, then equilibrium shifts to the left (less molecules) and becomes lighter
  Pressure is decreased:
    Initially lightens the solution, then equilibrium shifts to the right (more molecules) and becomes darker
  This can be demonstrated with a simple syringe

## Slide 23: 7.2.3 – Change in Temperature
Consider whether ∆H of the forward reaction is positive or negative
A reversible reaction has a enthalpy change equal and opposite for each direction (forward and reverse)
When temperature is increased, the equilibrium position will shift in the direction that will tend to lower the temperature (endothermic direction)
When the temperature is decreased, shifts toward the exothermic direction

## Slide 24: 7.2.3 – Effect of Temp on N2O4(g)
Nature of forward reaction (sign of ∆H) | Change in temperature | Shift in the position of equilibrium | Effect on value of Kc
∆H > 0 | Increase | To the right | Kc increases
∆H > 0 | Decrease | To the left | Kc decreases
∆H < 0 | Increase | To the left | Kc decreases
∆H < 0 | Decrease | To the right | Kc increases
For the same reaction:
  N2O4(g) ⇌ 2NO2(g) ∆H = + 57 kJ mol-1
  colorless brown
Decomposition is endothermic
  If put in an ice bath, color will get lighter
  If put in a hot water bath, color will get darker

## Slide 25: Break – Next Class:
7.2.4 State and explain the effect of a catalyst on an equilibrium reaction. (3)
7.2.5 Apply the concepts of kinetics and equilibrium to industrial processes. (2)

## Slide 26: 7.2.4 – Effect of a Catalyst
7.2.4 State and explain the effect of a catalyst on an equilibrium reaction. (3)
A catalyst is a substance that increases the rate of a chemical reaction by providing an alternative reaction pathway of lower activation energy (Ea)
Industrially catalysts are of significance, as they allow reactions to occur at reasonable rates under milder, and therefore more economic, conditions

## Slide 27: 7.2.4 – Catalyst – ∆ in equil or Kc
Catalysts have no effect on the position of equilibrium
The rates of both the forward and reverse reactions are lowered by providing an alternative pathway
There is no change in the Kc value either
The real advantage of a catalyst is that it reduces the time required for the equilibrium to be established.

## Slide 28: 7.2.4 – Catalyzed Reaction Review
The uncatalyzed reaction of ethanoic acid and ethanol takes weeks to reach equilibrium, with the addition of hydrogen ions (H+), it can be reached in a few hours
CH3CO2H(l) + C2H5OH(l) ⇌ CH3CO2C2H5(l) + H2O(l)
ethanoic acid ethanol ethyl ethanoate water
Reactants
Products
Potential Energy
Progress of Reaction
Ea without catalyst
Ea with catalyst

## Slide 29: 7.2.5 – Industrial Processes
7.2.5 Apply the concepts of kinetics and equilibrium to industrial processes. (2)
Many very important chemicals needed in industry are formed through reversible reactions in equilibrium
If we can take advantage of Le Chateliers Principle and manipulate the physical conditions large economic benefits may result.
The rate at which product is produced is also of economic concern.
  You will study the Haber and Contact Processes

## Slide 30: 7.2.5 – Haber Process for Ammonia
Nitrogen is of extreme importance for plant growth
Most plants cannot ‘fix’ nitrogen directly from air (which is 78% N2)
Only certain plants can convert nitrogen directly into a usable chemical with use of a bacteria present in their root nodules
To promote plant growth – N-compounds are added to crops as fertilizers (All use NH3)
  Urea – CO(NH2)2
  Ammonium sulfate – (NH4)2SO4
  Dihydrogen phosphate – NH4H2PO4

## Slide 31: 7.2.5 – Haber Process
Most plants use CH4 (natural gas), air, and water as starting materials.
If CH4 contains S, it will effect Ni catalyst, so removed
  CH4(g) + H2O(g) ⇌ CO(g) + 3H2(g) ∆H = +206 kJ mol-1
  Ni catalyst used at 750oC in ‘primary reformer’
The unwanted CO(g) formed is removed from the mixture in the ‘shift reactor’ by reaction with steam
N2 from the air is used but must be concentrated
  O2(g) (20% in air) is removed in the ‘secondary reformer’
    Now, for the production of ammonia:
  N2(g) + 3H2(g) ⇌ 2NH3(g) ∆H = -92 kJ mol-1

## Slide 32: 7.2.5 – Materials:
So what needed?
  CH4 (Sulfur removed)
  Steam
  Ni (as catalyst for CH4 and H2O)
  N2 from air (O2 removed from mixture)
What must be removed?
  S from CH4
  O2 from air
  CO from products of primary reformer

## Slide 33: 7.2.5 – Haber Process Diagram
CH4(g), H2O(g), N2(g), ½O2(g)
N2(g), CO(g), 2H2(g), H2O(g)
N2(g), 3H2(g)
CO(g) + H2O(g)  CO2(g) + 3H2(g)
N2(g), 3H2(g)
Fe catalyst
400oC
Cu catalyst
220oC
N2(g) + 2H2(g) ⇌ 2NH3(g)
Fe catalyst, 450oC
15% conversion
N2(g), 3H2(g)
cooled
condenser
air, etc
removal of ammonia
2NH3(l)
N2(g) + 2H2(g) + 2NH3(l)
reaction vessel
compressed to 250 atm
CO2(g) absorbed into K2CO3(aq)
two-stage shift reactor
primary and secondary reformers
CH4(g) + H2O(g)
CO(g) + 3H2(g)
½O2(g) + H2(g)
H2O(g)

## Slide 34: 7.2.5 – Haber Process Conditions
The conditions used in the Haber process are set using the Principles of Le Chatelier to achieve a satisfactory yield of ammonia at a reasonably economic rate
  N2(g) + 3H2(g) ⇌ 2NH3(g) ∆H = -92 kJ mol-1
The highest yield is produced using
  High pressures (favors less molecules)
  Low temperatures (favors exothermic reaction)
But, economically, it’s better to increase the rate
  High temperature, high pressure, in the presence of a catalyst

## Slide 35: 7.2.5 – Haber Choice of Pressure
For reasons discussed in 7.2.3, the choice of a high pressure will favor the side of equilibrium containing less moles of gas
  N2(g) + 3H2(g) ⇌ 2NH3(g) ∆H = -92 kJ mol-1
  4 moles in reactants vs. 2 moles in products
Also favored for kinetic reasons and most industrial plants operate at 200-250 atm’s (some +1000 atm)
  Higher pressure reaction vessels are very expensive as special chromium steel is used
  The decision is made by balancing the high initial costs against eventual profit of increased yield

## Slide 36: 7.2.5 – Haber Choice of Temperature
The process is exothermic, so lowering the temperature would favor the products:
    N2(g) + 3H2(g) ⇌ 2NH3(g) ∆H = -92 kJ mol-1
By raising the temperature, you would assume it would result in less ammonia in the equilibrium mixture
There are three reasons why temperature is raised:
  Low temp = slow reaction
  The catalyst used has an optimum operating temperature
  Ammonia can be condensed, N2 and H2 reused and not wasted, so low yield is a small concern

## Slide 37: 7.2.5 – Haber, use of catalyst
Uses a catalyst of freshly produced, finely divided iron
  Produced by reduction from Fe3O4 (magnetite)
  Used because it reduces the time to reach equilibrium
A promoter (which improves the performance of a catalyst) is often used: molybdenum, potassium oxide, aluminum oxide, potassium hydroxide
A typical industrial plant operates at 250 atm and 450oC and produces a conversion to ammonia of about 15%. Ammonia can be removed and the process continues.

## Slide 38: 7.2.5 – Haber Mechanism on Iron
Through the mechanism of chemisorption, N2 and H2 molecules dissociate into their ions on the iron surface, speeding up the reaction

## Slide 39: 7.2.5 – Haber Process Diagram
CH4(g), H2O(g), N2(g), ½O2(g)
N2(g), CO(g), 2H2(g), H2O(g)
N2(g), 3H2(g)
CO(g) + H2O(g)  CO2(g) + 3H2(g)
N2(g), 3H2(g)
Fe catalyst
400oC
Cu catalyst
220oC
N2(g) + 2H2(g) ⇌ 2NH3(g)
Fe catalyst, 450oC
15% conversion
N2(g), 3H2(g)
cooled
condenser
air, etc
removal of ammonia
2NH3(g)
N2(g) + 2H2(g) + 2NH3(l)
reaction vessel
compressed to 250 atm
CO2(g) absorbed into K2CO3(aq)
two-stage shift reactor
primary and secondary reformers
CH4(g) + H2O(g)
CO(g) + 3H2(g)
½O2(g) + H2(g)
H2O(g)

## Slide 40: 7.2.5 – Contact Process for H2SO4
Sulfuric acid (H2SO4) is the single most produced chemical world-wide and is produced through the contact process.
150,000,000 tons are manufactured each year for:
  Fertilizers
  Paints and pigments
  Detergents and soaps
  Dyestuffs
There are three stages to the contact process

## Slide 41: 7.2.5 – Contact Process Diagram
V2O5 catalyst
SO2(g) + ½O2(g) SO3(g)
Waste heat
600oC
SO2(g) production
three-stage converter
S(g) + O2(g)
SO2(g)
1000oC
98% H2SO4
500oC
400oC
Slightly above atmospheric pressure
absorber
Unreacted SO2(g) is removed and N2(g) is vented to the atmosphere
H2O(l)
SO2(g), air
Useful heat converted to steam
S(s), air
SO3(g) + H2O(l)
H2SO4(l)

## Slide 42: 7.2.5 – Contact Process State 1
Sulfur is burned in air at 1000oC
  S(s) + O2(g)  SO2(g)

## Slide 43: 7.2.5 – Contact Process Stage 2
Sulfur dioxide produced is then mixed with more air and passed over vanadium (V) oxide, V2O5 at 450oC
  2SO2(g) + O2(g) ⇌ 2SO3(g) ∆H = -197 kJ mol-1
This step is known as the Contact Step and is reversible (in equilibrium)
Shifted to the right by the addition of an excess of air – about 3x what is necessary
Le Chateliers Principle suggests the highest yield of products would be at high pressure, low temperature
  Once again, low temps = slow rates
  The catalyst is only useful above 400oC

## Slide 44: 7.2.5 – Contact Pressure Continued
Therefor a starting temperature of 450oC is used for each bed, but the exothermic process raises that temperature several hundred degrees
So, the gases are cooled back down to 450oC before passage onto the next bed
This conversion produces a 99.5% conversion from SO2 to SO3
Given the high rate of conversion (and cost of raising pressure) the reaction is run at 1-2 atm

## Slide 45: 7.2.5 – Contact Process Stage 3
Finally, the SO3 produced is dissolved in 98% sulfuric acid and water is added
  This is done to avoid the potentially violent and highly exothermic reaction if the gas was directly passed into water
SO3(g) + H2SO4(l)  H2S2O7(l)
H2S2O7(l) + H2O(l)  H2SO4(aq)